## Slide 1: A Laboratory to Teach Laser and Atomic Physics
Joseph E. Wiest
West Virginia Wesleyan College
AAPT Conference – Cincinnati 2017

## Slide 2: Course Description
Name: Electro-Optics (Laser Physics)
Number: PHYS 305L
Level: Junior
Time: Three hours per week
Text: “ A Laser Laboratory Guidebook”, Joseph E. Wiest
Pre-requisite: PHYS 210 Light and Atomic Physics
When offered: Each semester
Enrollment: 12 – 14 per semester
Founding date: About 1985

## Slide 3: Pertinent Physics Principles to Be Taught
Quantum oscillator model
Quantum atomic model
Nuclear shell model
Doublet and hyperfine structure of the atom
Physical optics concepts
Operating principles of gas, solid state, and dye lasers
Molecular structure
Molecular dynamics
Bethe-Weizsacker mass equation/nuclear stability

## Slide 4: Experimental Objectives
History, development, and applications of the laser
Doublet and hyperfine structure of the alkali metal elements
The acousto-optic effect
Bond strength of the linear molecule
The pumped tunable dye laser
Raman effect in polymers
Frequency doubling in crystals
Stable isotopes of elements

## Slide 5: The Ruby Laser

## Slide 6: Helium-Neon Lasers

## Slide 7: The Nitrogen Gas and Liquid Dye Lasers

## Slide 8: The AlGaAs Tunable Diode Laser

## Slide 9: The External Grating Tunable Diode Laser

## Slide 10: The Carbon-dioxide Laser

## Slide 11: Nd-YAG and InGaN Lasers

## Slide 12: The Ruby Laser Experiment – 693 nm

## Slide 13: Rubidium Experiment – 780 nm and 795 nm

## Slide 14: Cesium Experiment -- 852 and 894 nm

## Slide 15: The Iodine Molecular Bond Experiment

## Slide 16: ND-YAG Excitation of the Iodine Molecule

## Slide 17: The Krypton Optogalvanic Experiment

## Slide 19: The Temperature-Tunable Diode Laser
Cathode
Anode

## Slide 20: Calibration of the AlGaAs Tunable Laser
Chart: 
| 12.07 | 14.14 | 16.100000000000001 | 18.2 | 20.25 | 22.18 | 24 | 26.22 | 28.4 | 30.09 | 32.94 | 34.08 | 36.04 | 38.130000000000003 | 40.72 | 42.15 | 44.3 | 46.02 | 48.3 | 50.1 | 52.4 | 54.2 | 56.09 | 58.1 | 60 | 62.15 | 64.010000000000005 | 66.12 | 67.849999999999994
 | 779.082 | 779.205 | 779.338 | 779.573 | 779.696 | 779.696 | 779.942 | 779.942 | 779.942 | 780.065 | 780.065 | 780.188 | 780.311 | 780.311 | 780.311 | 780.311 | 780.557 | 780.68 | 780.68 | 780.68 | 780.926 | 780.926 | 781.048 | 781.048 | 781.048 | 781.048 | 781.048 | 781.171 | 781.171

## Slide 21: Rubidium 780 nm Line Data
Chart: 
| 46.89 | 47 | 47.07 | 47.16 | 47.24 | 47.33 | 48.46 | 48.53 | 48.6 | 48.66 | 48.73 | 48.8 | 48.9 | 49.01 | 49.11 | 49.21 | 49.58 | 49.71 | 49.78 | 49.82 | 49.86 | 49.89 | 49.95 | 49.99 | 50.05 | 50.13 | 50.2 | 50.28 | 50.34 | 50.4 | 50.5 | 50.58 | 50.64 | 50.75 | 50.83 | 50.88 | 50.96
 | 0.32 | 0.38 | 0.4 | 0.43 | 0.34 | 0.3 | 0.37 | 0.6 | 0.68 | 0.71 | 0.68 | 0.6 | 0.4 | 0.3 | 0.29 | 0.29 | 0.3 | 0.32 | 0.36 | 0.6 | 0.87 | 0.81 | 1.15 | 1.51 | 1.45 | 1.24 | 0.87 | 0.52 | 0.54 | 0.58 | 0.94 | 1.03 | 0.9 | 0.61 | 0.48 | 0.38 | 0.35
Laser Injection Current (mA)
Intensity (mV)

## Slide 22: Rubidium 795 nm Line Data
Chart: Injection Current (mA)
| 65.22 | 65.290000000000006 | 65.400000000000006 | 65.45 | 65.5 | 65.55 | 65.61 | 65.62 | 65.650000000000006 | 65.680000000000007 | 65.73 | 65.77 | 65.819999999999993 | 65.84 | 65.91 | 65.989999999999995 | 66.02 | 66.13 | 66.17 | 66.27 | 66.31 | 66.34 | 66.38 | 66.41 | 66.45 | 66.47 | 66.540000000000006 | 66.59 | 66.650000000000006 | 66.72 | 66.81 | 66.92
 | 1.28 | 1.3 | 1.31 | 1.31 | 1.32 | 1.36 | 1.47 | 1.47 | 1.44 | 1.42 | 1.35 | 1.33 | 1.32 | 1.32 | 1.32 | 1.33 | 1.33 | 1.49 | 1.51 | 1.4 | 1.39 | 1.39 | 1.36 | 1.37 | 1.4 | 1.38 | 1.33 | 1.33 | 1.33 | 1.33 | 1.33 | 1.33

## Slide 23: Hyperfine Splitting of the 852 nm Line in Cs
Chart: 
| 84.6 | 84.7 | 84.8 | 84.9 | 85 | 85.1 | 85.2 | 85.300000000000097 | 85.400000000000105 | 85.500000000000099 | 85.600000000000094 | 85.700000000000102 | 85.800000000000097 | 85.900000000000105 | 86.000000000000099 | 86.100000000000094 | 86.200000000000102 | 86.300000000000097 | 86.400000000000105 | 86.500000000000199 | 95 | 95.1 | 95.2 | 95.3 | 95.4 | 95.5 | 95.6 | 95.7 | 95.8 | 95.899999999999906 | 95.999999999999901 | 96.099999999999895 | 96.199999999999903 | 96.299999999999898 | 96.399999999999906 | 96.499999999999901 | 96.599999999999895
 | 62 | 65 | 71 | 97 | 120 | 134 | 149 | 165 | 183 | 201 | 209 | 218 | 206 | 187 | 153 | 120 | 92 | 75 | 65 | 62 | 47 | 54 | 64 | 96 | 122 | 138 | 147 | 151 | 153 | 148 | 141 | 132 | 120 | 94 | 74 | 60 | 51
Piezo Voltage (V)
Intensity
(mV)
852.338 nm

## Slide 24: Hyperfine Splitting of the 894 nm Line in Cs
Chart: 
| 48.5 | 48.55 | 48.6 | 48.65 | 48.7 | 48.75 | 50.9 | 50.95 | 51 | 51.05 | 51.1 | 51.15 | 51.2
 | 39.6 | 44 | 48.2 | 50.6 | 44.8 | 40.9 | 41 | 43 | 47.1 | 50.6 | 48.7 | 43.9 | 42
Intensity (mV)
Injection Current (mA)

## Slide 25: Nuclear Energy Levels – Maria Goeppert Mayer – for 1H , 7Li , 23Na , 39K , 85Rb , 133Cs
8 Cs + 22 above 5 Cs 1g7/2
8 Rb 10 Cs 10 Cs 1g9/2
2 Rb 2 Cs 2 Cs 2P1/2
6 Rb 6 Cs 5 Rb 6Cs 1f5/2
4 Rb 4 Cs 4 Rb 4Cs 2P3/2
8 Rb 8 Cs 8 Rb 8Cs 1f/7/2
4 K 4 Rb 4 Cs 3 K 4 Rb 4 Cs 1d3/2
2K 2 Rb 2 Cs 2 K 2 Rb 2 Cs 2S1/2
4 Na 6 K 6 Rb 6 Cs 3 Na 6 K 6 Rb 6 Cs 1d5/2
1 Li 2 Na 2 Rb 2 Cs 2 Na 2 K 2 Rb 2 Cs 1P1/2
4 Li 4 Na 4 K 4 Rb 4 Cs 1 Li 4 Na 4 K 4 Rb 4 Cs 1P3/2
2 Li 2 Na 2 K 2 Rb 2 Cs 1 H 2 Li 2 Na 2 K 2 Rb 2 Cs 1S1/2
Neutrons Protons

## Slide 26: Rubidium - 85 Doublet and Hyperfine Levels
Atomic energy state of J = 1/2 , Nuclear state = 5/2 :
F = Net atomic state = I ( Nuclear state ) + - J ( Atomic state ) F =
= 5/2 +- 1/2 = 2 , 3 F = 4
3 Atomic energy state of J = 3/2 : 5P3/2 2
5P1/2 3 1
F = 5/2 +- 3/2 = 1 , 2 , 3 , 4 780 nm 2
795 nm 3 3
Transition rules: 5S1/2 ΔL = +- 1 ΔF = 0 , +- 1
2 2

## Slide 27: Cesium -- 133 Doublet and Hyperfine Levels

## Slide 28: Hyperfine Energy Level Splitting (Steck)
The Hamiltonian
Hhfs = AhfsI◦J +
Bhfs (3(I◦J)2+3/2(I◦J)-I(I+1)J(J+1))
2I(2I-1)J(2J-1)
Ahfs = Magnetic dipole constant
Bhfs = Electric quadrupole constant
(J>1/2)

## Slide 29: Calculating Hyperfine Energy Splitting (Steck)
∆Ehfs = (1 /2) AhfsK + Bhfs {[(3/ 2)[K(K + 1) − 2I(I + 1)J(J + 1)]/[ 2I(2I − 1)2J(2J − 1)]}
where K = F(F + 1) − I(I + 1) − J(J + 1)

## Slide 30: Hyperfine Splitting Measurements
Rubidium : Measurement (nm) Accepted Value (nm) % Diff
(Rb-85) 780.652 780.238 .0531
780.712 780.244 .0600
794.959 794.975 .00201
794.965 794.982 .00214
Cesium: 852.338 852.335 .000352
(Cs-133) 852.361 852.357 .000469
893.722 894.579 .0958
893.744 894.603 .0960

## Slide 31: Spectrum of Iodine Molecule Excited by Frequency-Doubled Nd:YAG Laser

## Slide 32: The Birge – Sponer Plot
Chart: Birge - Sponer Plot for Iodine
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
 | 2.298 | 2.159 | 2.125 | 1.97 | 2.27 | 1.901 | 1.862 | 2.147 | 2.095 | 2.016 | 1.996

## Slide 33: Calculations from the Data; Harmonic Oscillator Model
K = m ( 2πcω0 )2
= 127x1.6605x10-27 /2 x (2π x 2.9979x108 x 2.198x104)2
= 180.7 N/m (Our result)
K = 172.1 N/m (Bayram And Freamat)

## Slide 34: Raman Scattering (Nylon) – Rayleigh Peak
Chart: Wavelength(Å)
| 3250 | 3251 | 3252 | 3253 | 3254 | 3255 | 3256 | 3257 | 3258 | 3259 | 3260
 | 3.07 | 3.57 | 3.02 | 6.67 | 18.34 | 22.98 | 12.71 | 3.91 | 1.9 | 1.24 | 1.65

## Slide 35: Raman Scattering (Nylon) – Stokes Peak
Chart: Wavelength(Å)
| 3459 | 3459.5 | 3460 | 3460.5 | 3461 | 3461.5 | 3462 | 3462.5 | 3463 | 3463.5 | 3464
 | 0.21 | 0.22 | 0.25 | 0.28 | 0.38 | 0.41 | 0.3 | 0.27 | 0.21 | 0.21 | 0.2

## Slide 36: Raman Scattering (Nylon) – Anti-Stokes Peak
Chart: Anti-Stokes Peak
| 3056 | 3055.5 | 3055 | 3054.5 | 3054 | 3053.5 | 3053 | 3052.5 | 3052 | 3051.5 | 3051
 | 0.21 | 0.22 | 0.23 | 0.25 | 0.31 | 0.25 | 0.22 | 0.2 | 0.2 | 0.21 | 0.2

## Slide 37: The Stable Isotopes of Krypton
Chart: Injection Current [mA]
| 61.7 | 61.8 | 61.9 | 62.2 | 62.5
 | 0.2 | 0.6 | 0.2 | 0.4 | 0.2

## Slide 38: WV Wesleyan Physics Senior Class 2016-2017

## Slide 39: Conclusions
Course reviews and reinforces concepts of previous year classes in light, atomic, and nuclear physics.
Students are prepared to do funded summer research work on our campus or other involving laser/atomic physics.
Graduates report experience from course has facilitated good graduate research assignments.
Graduates report good use of concepts and techniques of course in both physics and engineering graduate study.
Hands-on experience and research techniques encountered in course have provided excellent preparation for the year of senior research.

## Slide 40: Acknowledgements
NASA – WV Space Grant Consortium
West Virginia Wesleyan College
Aaron Weaver, (Wesleyan 2015, now grad Physics at WVU)
Mackenzie Robatin and Gabrielle Cox, Summer Research 2017
Students in the Electro-Optics Classes of 1993 to 2017
SURE Grant Program
Robert Grose for machining; Tracey Delaney for computer and technical help
Dr. G.S. Hurst, Oak Ridge National Laboratory

## Slide 41: References
1. S.B.Bayram and M.V.Freamat, “Simple Laser-Induced Fluorescence Setup to Explore Molecular Spectroscopy”, Compadre.Org /advlabs/bfy/files/W31, 1-8 (2012).
2. Livesey, Derek, Atomic and Nuclear Physics (Ginn and Blaisdell, Toronto, 1966).
3. Serway, Moses, Moyer, Modern Physics (Thomson-Brooks/Cole, Belmont, CA, 2005).
4. Steck, Daniel, Dept. of Physics, Univ. of Oregon, Rubidium 85 D Line Data, 2013.
5. Steck, Daniel, Los Alamos National Laboratory, Cesium 133 D Line Data, 2003.
6. Derek Eastham, Atomic Physics of Lasers (Taylor and Francis, 1986).
7. H.Haken and H.C. Wolf, Atomic and Quantum Physics (Springer-Verlag, 1984).
8. C.J. Foot, Atomic Physics (Oxford Press, 2005).
9. David Van Baak, Physics Dept., Calvin College, 1993.