## Slide 1: Zeeman Effect Experiment with High-Resolution Spectroscopy for Advanced Physics Laboratory
Dr. Andrew Taylor
Physical Sciences, Inc. Andover, MA
Dr. Oleg Batishchev and Alex Hyde
Department of Physics, Northeastern University, Boston, MA
January 9th, 2018
The Wonderful World of AJP

## Slide 2: Abstract
An experiment studying the physics underlying the Zeeman effect and Paschen-Back effect is developed for an advanced physics laboratory. We have improved upon the standard Zeeman effect experiment by eliminating the Fabry-Perot etalon, so that virtually any emission line in the visible spectrum can be analyzed. Emitted light from a ~1T magnet is analyzed by a Czerny-Turner spectrograph equipped with a small-pixel imaging CCD. The experiment was taught as part of the Principles of Experimental Physics course at Northeastern University to a combination of graduate/undergrad students. Zeeman’s original sodium experiment is recreated, and the splitting of argon and helium lines is measured as a function of field strength. The students analyze the proportionality of the splitting magnitude to both the B-field strength and lambda squared. The Bohr magneton is calculated and compared to theory. Student feedback is positive, citing the ability to experimentally witness a quantum mechanical effect.
A. Taylor, A. Hyde, and O. Batishchev, Am. J. Phys. Vol. 85, No. 8 (2017).
Notes: A permanent magnet Holder for variable B-field strength

## Slide 3: History of the Zeeman Effect
1896: Pieter Zeeman observed a widening of the sodium D line in the presence of a magnetic field (normal Zeeman effect).
1897: Zeeman observed the line through a polarizer; he found two outer circularly-polarized peaks and a central plane-polarized peak; verified Lorentz’s theoretical predictions.
1898: Thomas Preston observed quartet pattern of lines in a magnetic field (Anomalous Zeeman effect).
1902: Paschen, Runge, and others fine Anomalous Zeeman effect patterns of six, nine, eleven, etc. in atomic spectra.
1925: Schödinger formulates wave equation
1925: Pauli and Heisenberg formulate nascent quantum mechanics to explain the Anomalous Zeeman effect
1926: Uhlenbeck and Goudsmit, Bichowsky and Urey independently discover the intrinsic spin of the electron,
In case you missed it in your Modern Physics class…
Notes: A permanent magnet Holder for variable B-field strength

## Slide 4: Quantifying the Zeeman Effect
An external magnetic field B exerts a torque on an electron’s magnetic dipole µ and shifts the energy of the atomic level from the non-perturbed energy by
where is the Landé g-factor, is the Bohr magneton, and is the projection of the total angular momentum J = L + S.
The change in wavelength from a small change in energy is
Substituting and ,
For practical laboratory settings, pm.
Image sourced from:
http://hyperphysics.phy-astr.gsu.edu/hbase/quantum/zeeman.html
Notes: B=1.07 T was maximum for the Pasco tubes.
Done for five He I lines and one Ar I line

## Slide 5: Zeeman Effect in Physics Teaching Lab
Understanding the Zeeman effect is important for historic and current research
Experiments introducing the effect are widely used in physics laboratory curricula
Common approach utilizes electromagnets and Fabry-Perot etalon
Requires Reflectivity to resolve splitting of lines
Usually measures only a few spectral lines
Electromagnets and/or etalon require liquid cooling to maintain performance
Replaced Fabry-Perot with high-resolution spectroscopic system that allows measuring the entire spectrum
Replaced electromagnet with permanent magnets with 1 T
Example: Zeeman Experiment at MIT Junior Physics Lab
Notes: With R verified, I applied the instrument towards measuring the Zeeman Effect…
In the process, I developed a new experiment which showcases the strengths of this system.
Water cooled, only run for short periods of time. Room maintained at constant temp due to etalon

## Slide 6: McPherson M216 Spectrometer
Made by McPherson in 1960s
Used at Harvard Center for Astrophysics
Donated to NEU Plasma Lab in 2014
Asymmetrical Czerny-Turner design
= 1 m focal length with 1200 g/mm grating
Large 8” collecting and 12” focusing mirrors
Originally designed for 35 mm film
Was retrofitted to deliver high spectral resolution in UV—NIR range with new CMOS camera and collecting optics
Side view of M216 installed in the NEU Plasma Lab
Notes: The spectrometer used for this new approach is a M216…
Retrofitting included four features…
Less dense grating gives a broader spectral range

## Slide 7: Initial Viability Test of Spectroscopic System
Tested Resolution in measuring Zeeman Effect using a simple proof-of-concept
Pasco Spectral Tube 50-W discharge tube and 125 V Power Supply
Modified a Pasco Spectral Tube power supply to lay flat, and two attached N50 neodymium magnets created a T field at center of tube
Optical fiber pointed in center of field
Observed Zeeman triplet splitting of the He I 706 nm line
  MU1403 camera, 5 um slit
  Side peaks approx. half of center peak
Initial proof-of-concept setup
Initial spectrum of Zeeman Effect
Notes: A permanent magnet Holder for variable B-field strength

## Slide 8: Permanent Magnet Holder for Zeeman Effect
Magnet Holder was designed by Prof. Batishchev
Machined by NEU machine shop
Two 8” arms each loaded with a 2” N52 neodymium permanent magnet, remanence T at surface
  Threaded for 1 mm/rotation travel
  Handles added and marked
Rotation of arms in the body varies separation distance
Upper and lower openings through which the light source is placed
Side opening notched for mm-measurements
Sturdy wooden frame cut, assembled, and installed on optical bread board table
3D-printed tube stop on top and bottom to secure light source
Holder body and arm
Assembled Holder in frame
Notes: A permanent magnet Holder for variable B-field strength

## Slide 9: Calibration of B-Field Strength Measurements
Measured Field Strength across the magnet face at various
Placed the sensor tip of an Alpha Labs gaussmeter on a moveable stage
Made multiple measurements at mm to determine accuracy
  T
For a given , measured every mm, starting at
  Ran calibration 3x to eliminate possible sensor tip misalignment
Achieves 1.19 T in center
Approx. uniform across face of magnets
Magnetic field as a function of radial distance from the center for varied
Magnetic field at as a function of separation distance
Notes: A permanent magnet Holder for variable B-field strength
Gaussmeter didn’t *quite* fit through the long, narrow opening, and so the tip would rotate and measure lower flux

## Slide 10: Light Source and Collection Optics
Continued to use Pasco Spectral tubes
Used optical fibers for emission collection from discharge to M216
Cannot bring fiber directly into Magnet Holder, built two-lens collimator
  Back lens selected to match the NA of the fiber
  Front lens selected to collect light from smallest possible
Left: Collimator for collected emission
Right: end tube into which the collimator fit
Retrofitted M216 entrance slit with optical fiber attached
Notes: A permanent magnet Holder for variable B-field strength

## Slide 11: UV-VIS Spectroscopic Systems
Utilized two spectroscopic systems
1:Ocean Optics USB4000 for broad UV—VIS coverage
  3648 pixels at 2 nm/pix resolution
2: McPherson spectrometer with Touptek MU1403 14 MP Camera and customized LabVIEW interface
  4096 x 3286
  ~350-1100 nm spectral range
  1.4 μm pixel
  LabVIEW VI controls integration time, gain, color, etc.
  Modified it to integrate image into 1D spectrum and to crop & integrate a small ROI
Notes: Dispersion is 8.3 A/mm
MU1403 is color, Jenoptik is only B&W but with better sensitivity

## Slide 12: Determination of Spectral Lines
Helium and Argon ultimately chosen as the sources for Zeeman effect experiment
Single-isotope elements with >99.6% purity
Large number of bright lines across entire UV—NIR spectrum
Utilized closely-spaced peaks at 587, 706, 751, and 811 nm to calibrate the per-pixel resolution
  pm/pix
  Extrapolated resolution for other wavelengths from linear curve
He I and Ar I spectra from USB4000
Calibration using closely-spaced peaks
Notes: B=1.07 T was maximum for the Pasco tubes.
Done for five He I lines and one Ar I line

## Slide 13: Zeeman Effect in Singlets
Measured Zeeman splitting of a line as -field varied from 0.5—1.07 T in 0.1 T increments
Distance values of , respectively
Measured in He I 501 and 667 nm, and Ar I 811 nm singlets
Schematic of Zeeman splitting in He I 667 nm singlet transition
He I 667 nm at 1.07 T
Image taken from PHYS5318 lab manual.
Notes: B=1.07 T was maximum for the Pasco tubes.
Done for five He I lines and one Ar I line

## Slide 14: Zeeman Effect in Triplets
In the strong field limit, and decouple and interact independently with the field
All transitions converge to exhibit normal Zeeman triplet with
Effect appears when
In helium this occurs around B ~ 0.4 T
The limit observed in He I 388, 447, 587, and 706 nm triplet lines
Schematic of Zeeman splitting in He I 706 nm triplet transition at Paschen-Back Limit
He I 587 nm at 1.07 T
H. Odenthal et al. Physica,113C 203-216 (1982).
Image taken from PHYS5318 lab manual.
Notes: B=1.07 T was maximum for the Pasco tubes.
Done for five He I lines and one Ar I line

## Slide 15: Study of B-field Dependence
Observed Zeeman splitting of a line as -field varied in 0.1 T increments from T
Collected 5x images for each to gather experimental uncertainty in
Analyzed pixel spacing for left and right peak via LabVIEW cursor, averaged for
Converted into via measured
Graphed vs. for six He I VIS lines and one Ar I line
From lines, calculated Bohr magneton value with average accuracy of 10%
vs. for Ar I 811 nm
Bohr Magneton calculation accuracy
vs. for He I 587 nm
Notes: B=1.07 T was maximum for the Pasco tubes.
Done for six He I lines and one Ar I line

## Slide 16: Study of λ2 Dependence
Unique Ability of System
Spectroscopic System has unique ability to measure the dependence of Zeeman splitting
Analysis is available for virtually any line in the VIS spectrum
Used six He I lines from 388—706 nm at T
  Bohr magneton calculation is more accurate and precise using this new method
vs. for He I discharge at 1.07 T
Notes: Proportional to B with wavelength fixed, but also proportional to lambda^2 with B fixed.
This system has the unique ability to study that proportionality.

## Slide 17: Anomalous Zeeman Effect in Argon
Most argon lines exhibit the Anomalous Zeeman effect (not Paschen-Back)
Triplet patterns of with , e.g. Ar I 696 nm
Quartet patterns of , e.g. Ar I 810 nm
Sextet patterns of , e.g. Ar I 912 nm
Excellent candidate to teach the Anomalous Zeeman splitting, either in conjunction with helium or as a separate experiment
Ar I 696 nm at 1.07 T
Ar I 810 nm at 1.07 T
Ar I 912 nm at 1.07 T
Notes: B=1.07 T was maximum for the Pasco tubes.
Done for five He I lines and one Ar I line

## Slide 18: Improvements and NIR Extension
Increasing groove density will increase per-pixel resolution but decreases the longest viewable wavelength
Maximum Zeeman split magnitude decreased from current magnitude by
where is the ratio between 1200g and new grating
  The bright He I 1083 nm triplet represents ~135% increasing in Zeeman split over He I 706 nm
  Two systems used to measure lines
Princeton Instruments IsoPlane 320 with 1200-g/mm grating and 20 m pixels
McPherson M216 + MU1803-FL camera with 1.85 m pixels
A. Taylor and O. Batishchev, Can. J. Phys. 95: 993-998 (2017).
Notes: B=1.07 T was maximum for the Pasco tubes.
Done for five He I lines and one Ar I line

## Slide 19: Designing the APL Experiment
Experiment created using the Magnet Holder, USB4000 & M216 + MU1403 spectrometers, and helium & sodium tubes
Designed it around calculating from both - and -dependencies of the normal Zeeman and Paschen-Back effects
  Re-create Zeeman’s original sodium lamp experiment, showing widening of Sodium D line
  Study -dependence using three helium lines (He I 587, 667, 706 nm)
  Study -dependence using four helium lines at T (He I 587, 667, 706, and 1083 nm)
Designed lab manual and lab report grade guide
Sodium lamp used to re-create Zeeman’s original findings
Notes: B=1.07 T was maximum for the Pasco tubes.
Done for five He I lines and one Ar I line

## Slide 20: Teaching the APL Experiment
Taught experiment for PHYS5318 – Introduction to Experimental Physics at Northeastern University in Spring 2017
Total of 14 students, both grad and undergrad, across 14-week semester
Two 3-hour lab sessions
  Generally 1st to take broad He I and Na I spectra, high-res Sodium D broadening, and some high-res He I Zeeman effect spectra
  2nd to take the rest of the He I spectra and analyze the pixel spacing between peaks
  Graphing, calculation of , and report done outside of class time
Overall positive student outcome with the experiment
High comprehension of what to do, mixed comprehension of why it was done
Best comment: “I’ve never done an experiment that explained Quantum Mechanics so well! I think I finally get it!”
Improvements: start the lab manual with the detailed theory; cut out one or two He I parts; provide more motivation for finding two ways
Notes: B=1.07 T was maximum for the Pasco tubes.
Done for five He I lines and one Ar I line